## Slide 1: Security Enhancements for Network Segregation
Henrik Ekholm

## Slide 2: Reason
Cyber Attacks against Industry networks are on the rise
Overall average increase in Cyberattacks 25% per quarter (2019 Q4 – 2020)
Manufacturing most with 156%
High impact on daily life
Last big sector not already secured

## Slide 3: Problem
Production Systems are notoriously hard to protect
Proprietary systems and protocols
  Hard to monitor
Sensitive machines
  Active probing can break systems
Time Critical response times
  Delays cause ripple effects
  Parallel running software can break processes

## Slide 4: Process
What can be done?
Proprietary systems and protocols
  No uncontrolled communication on network
Sensitive machines
  Rely on passive monitoring methods
Time Critical response times
  No extra software on devices

## Slide 5: Process
What can be done?
Proprietary systems and protocols
  No uncontrolled communication on network
    Segment
Sensitive machines
  Rely on passive monitoring methods
    Canary servers
    Log monitoring
Time Critical response times
  No extra software on devices
    Monitor communication instead

## Slide 6: How to organize
The Purdue Model

## Slide 7: Sorting
Adding all systems where they belong

## Slide 8: Logging
Data historian
Central Log Collection
Forwards relevant logs to Elastic pool
Time synchronized

## Slide 9: Sorting
Adding Data historian

## Slide 10: Segmentation
Firewalls
Firewall 1 controlled by Corporate IT
  Controls communication into Enterprise network
Firewall 2 controlled by plant Engineers
  Controls communication into Manufacturing network
No direct communication can happen unless both teams agree
DMZ communication can happen unilaterally

## Slide 11: Sorting
Implementing Firewalls

## Slide 12: Remote access to production
Jump Server
Single server that allows remote access
Access brokered by PAM solution

## Slide 13: Sorting
Adding Jump Server

## Slide 14: Warning System
Canary Server
Any change to server causes alarm
Decoy servers, as similar configuration as others in use at the site

## Slide 15: Sorting
Adding Canary

## Slide 16: Controlling outbound communication
sinkhole / proxy server
All requests sent from Manufacturing network rerouted
  If by IP, unexpected requests dropped at firewall
Whitelist is maintained for acceptable use
  Unacceptable requests dropped with no response

## Slide 17: Sorting
Adding Proxy/Sinkhole

## Slide 18: Operationalize
Running the system
SOC team playbook with
  Plant contacts
  Reaction to Canary alarm
  Log analysis
Infrastructure teams
  Server and network maintenance

## Slide 19: END, Questions?

## Slide 20
Data historian:
  osisoft-pi (as compatible with Siemens and Rockwell)
Jump server:
  Hardened Virtual or on-site windows machine.
  Beyond trust PAM also handles
  Access groups managed with Azure AD
Canary server
  Fortinets FortiDeceptor
  Depending on other servers in use, standard is windows 2008 server
Proxy/sinkhole (tarpit)
  Avamar as proxy
  DNS sinkhole usable for known bad sites already implemented on corporate level